EXHIBIT “D”

RIG #11- 1500 HP

## DRAWWORKS

Davis 1500-E (National 110 UE copy) with 2 – GE 752 DC Motors

Grooved for 1 3/8” Drill Line

WPT 235 Auxiliary Electric Brake

## DERRICK

Superior

142' High, Cantilever Mast

768,000# Static Hook Load Capacity

## SUBSTRUCTURE

Superior  with 768,000# casing capacity and 500,000 # setback capacity

21’ Rotary Beam Clearance

25' High Box on Box Type

POWER SOURCE

(3) - Caterpillar 3512C’s w/ 1365 KW generators

Ross Hill type 3 x 4 bay SCR House

## PUMPS

3-F-1600 Type 7 ½” x 12" Triplex Powered by 2-752 DC Motors each - 7500 psi working system

Low Pressure Mud Mixing System with Two 6” x 5” x 11” Centrifugal Pumps w/40 HP Electric Motors

## DRILL STRING

Drill Pipe - 4½" Grade S-135 / G-105 16.60, NC46 X-Hole with Hardband

Drill Collars – 6” - 6½” OD NC44 with Hardband

8" - 8"   OD 5"H90

Pipe Spinner:  J29 Varco Chain Type

## PREVENTERS

1- 13 5/8” Hydril type Annular wp 5000 psi

1- Schaffer style 13 5/8” 10,000 psi Double Rams

1-Shaffer style 13 5/8” 10,000 psi Single Ram

1-  4 1/16” manual valve, 1- 4” HCR valve, 2- 2 1/16” valves and 1- 2 1/16” check valve all 10,000 psi

1- CAD Type M Series, 6 Station Closing Unit with 20 - 11 Gallon Bottles and with 150 Gallon Reserve with remote

Choke Manifold-10,000 psi 4 1/16" x 3" with Two Adjustable 3 1/16’’Choke

## OTHER EQUIPMENT

350 ton Warrior Hydraulic top drive w/7500 psi circ rating

Columbia In-Sub Walking System with HPU

Crown Block – Superior – (7) 48" Sheaves,

Traveling Block – National Oilwell type 500 Ton

Weight Indicator - Type EB

Rotary -  27½" x 53¼"

Fuel Tank with Lubester – 15,000 Gallon

50 bbl trip tank

Wireline Unit  - .092 Line

Mud Tanks – Two Tank System, Round Bottom, 750 BBL with 5 Electric Agitators Plus 105 BBL Slugging Tank

Shakers  – 3 x Derrick 503 Type Linear Motion

Desander - Derrick, (2) 12" Cones with Southwest 6” x 5” x 11” Centrifugal Pump w/40 HP Electric Motor

Desilter - Derrick, (12) 4" Cones with Southwest 6” x 5” x 11” Centrifugal Pump w/40 HP Electric Motor

Degasser – Derrick Drilco type

OFI Basic Services

498 Barrel Drill Water Tank