EXHIBIT “D”

RIG #15 – 1000 HP

DRAWWORKS

D1000E Drawworks with 2-DC 752 Motors

Grooved for 1 ¼” Drill Line

424 Air Operated Water Cooled Aux-Brake

DERRICK

DSII

142’ Triple Derrick or 110’ Double

550,000# Static Hook Load with 10 Lines

SUBSTRUCTURE

DSII

12’6’’ Rotary Beam Clearance, 17' RKB

16’ Box On Box Substructure

POWER SOURCE

(2) Caterpiller 3512C’s W/ 1225 KW Generators

Ross Hill 3 Bay SCR House

PUMPS

(3) Emsco type F-1000 6¾" x 10" Triplex powered by one 752 DC motor

Low Pressure Mud Mixing System with Two 5" x 6" Centrifugal Pumps w/60 HP Electric Motors

DRILL STRING

Drill Pipe - 4½" Grade G-105 16.60, X-Hole with Hardband (±13,100’)

Drill Collars – 6” - 6½” OD NC44 with Hardband

Pipe Spinner

PREVENTERS

(1) Shafer Hydril 11" Annular w.p. 5000 psi

(1) NL Shafer 11" Type LWS 5000 psi Space Saver Double Rams

(1) CPC Closing Unit (4) Station 3000 psi with 25 HP Electric Motor with Triplex Pump (2) Air Pumps CS-01108,

(8) 10 Gallon Bladder Type Bottles with remote

Choke Manifold - 5000 psi 4" x 2" with two Adjustable Chokes

OTHER EQUIPMENT

Warrior 250 Ton Top Drive

Crown Block - DSII, (5) Sheaves

Traveling Block - YG-225-250 Ton - (5) 36” Sheaves

Cold start - QT 7.5

Weight Indicator - AOI

Rotary - 27½” x 53¼” 275

Air Compressors - (2) Quency 120 screw type

Air dryer OHD

Fuel Tank with Lubester - 8000 Gallon

Wireline Unit - Mathey Model GC3-B2 type, .092 Line

Mud Tanks - Two Tank System, Round Bottom 560 Barrels with Electric Agitators

2 Shaker - Derrick 504 Hyperpool Type Linear Motion

Desander - Brandt, (2) 12" Cones with Mission Magnum 5" x 6" Centrifugal Pump w/75 HP Electric Motor

Desilter - Brandt, (12) 4" Cones with Mission Magnum 5" x 6" Centrifugal Pump w/75 HP Electric Motor

Degasser – Derrick Drilco type

OFI Basic Services

315 Barrel Drill Water Tank

Hydraulic Walking System

Revised	9/19/2023