EXHIBIT “D”

RIG #16- 2000 hp

## DRAWWORKS

OIME 2000  with 2 – GE 752 DC Motors

Grooved for 1 3/8” Drill Line

Wichita 336 water cooled Auxiliary Brake

## DERRICK

DSI

150' High, Cantilever Mast

1,000,000# Static Hook Load Capacity

## SUBSTRUCTURE

DSI  with 1,000,000# casing capacity and 600,000 # setback capacity

26’ Rotary Beam Clearance

30' High Box on Box Type

POWER SOURCE

(3) - Caterpillar 3512C’s w/ 1365 KW generators

Omron Hill type 4 x 4 bay SCR House

## PUMPS

3-Weatherford MP-16 Type 7 ½” x 12" Triplex Powered by 2-752 DC Motors each - 7500 psi working system

Low Pressure Mud Mixing System with Two 8" x 6" Centrifugal Pumps w/ 75 HP Electric Motors

## DRILL STRING

Drill Pipe – 5” 19.5# S-135 NC50 WITH 4 ½” IF connections (±22,300’)

Drill Collars – 6” - 6½” OD NC44 with Hardband

8" – 8 1/2"   OD 6-5/8” REG

Pipe Spinner:  J29 Varco Chain Type

## PREVENTERS

1- 13 5/8” Hydril type Annular wp 5000 psi

1- Schaffer style 13 5/8” 10,000 psi Double Rams

1-Shaffer style 13 5/8” 10,000 psi Single Ram

1-  4” manual valve, 1- 4” HCR valve, 2- 2 1/16” valves and 1- 2 1/16” check valve all 10,000 psi

1- CAD Type M Series, 5 Station Closing Unit with 220 Gallon capacity with remote

Choke Manifold-10,000 psi 4" x 3" with Two Adjustable 3’’Choke

## OTHER EQUIPMENT

NOV TDS-11 500 ton top drive w/ AC VFD house and 7500 psi working pressure

Walking System with HPU

Crown Block – (7) 60" Sheaves,

Traveling Block – Oilwell  500 Ton

Weight Indicator - Type D

Rotary -  37½" x 500 ton

Fuel Tank (11,000 gallons) with Lubester –

trip tank (100 bbl)

Wireline Unit  - .092 Line

Mud Tanks – Two Tank System, Round Bottom, 1000 BBL with Electric Agitators Plus Slugging Tank

Shakers  – 3 x Derrick 514 Type Linear Motion

Desander - Swaco, (2) 12" Cones with Mission Magnum 5" x 6" Centrifugal Pump w/40 HP Electric Motor

Desilter - Swaco, (12) 4" Cones with Mission Magnum 5" x 6" Centrifugal Pump w/40 HP Electric Motor

Degasser – Swaco

OFI Basic Services

Drill Water Tank (500 bbl)

Revised	9/19/2023