EXHIBIT “D”                                           RIG #6 – 750 HP

DRAWWORKS

Brewster Model N4-A

Grooved for 1⅛" Drill Line

Parmac SR 22 Single Hydromatic Brake

DERRICK

Superior, 105’ high

10' 9" Rotary Beam Clearance, 13' RKB

275,000# Static Hook Load with 8 Lines

Mounted on Lee C. Moore Triaxle Trailer

POWER SOURCE

2-Caterpillar C-13 (Diesel) 830 Horsepower

2-Twin Disc Model F-11524-TCIL Torque Converters

Two Engine Split Oil Bath Compound

(1) Quincy Model 350 Air Compressors

PUMPS

1-Emsco F-1000 6¾" x 10" Triplex Powered by Cat C32 with National C-245-64 Torque Converters

1-Emsco F-1000 6¾" x 10" Triplex Powered by Cat C32 with National C-245-64 Torque Converters

Low Pressure Mud Mixing System with Two 5" x 6" Centrifugal Pumps w/60 HP Electric Motors

DRILL STRING

Drill Pipe - 4" OD 14.40# GradeG-105, 4” Full Hole with Hardband (±10,700’)

Drill Collars - 6"- 6¼" OD Slick NC44 with Hardband

Kelly - Omsco 5¼" x 36' Hex

Pipe Spinner - Varco SS10

Kelly Spinner - International

PREVENTERS

1-GK Hydrill 11” 900 Series Annular wp 3000#

1-NL Shaffer 11" Type LWS 3000# Space Saver Double Rams

1-CPC Closing Unit, (4 Station) 3000psi with 25 HP Electric Motor with CPC Model T10 Triplex Pump

(2) Air Pumps CS-01108, (8) 10 Gallon Bladder Type Bottles

Choke Manifold - 5,000 psi 4" x 2" with Two Adjustable Chokes

OTHER EQUIPMENT

Crown Block - Superior (5) 36" Sheaves

Traveling Block - 150 Ton Ideco UTB type, 4 Sheaves

Swivel - EMSCO LB200 - 200 Ton

Weight Indicator – Martin Decker Clipper

Rotary - 17½” x 44¼” RT 175

Generators - Two 410KW with 2-C15 CAT Tier 4 @ 626 H.P. each

Air Compressors – (2) Sullivan 300-DG-TE Screw Type

Fuel Tank with Lubester - 8000 Gallon

Wireline Unit - Mathey Model GC3-B2 type, .092 Line

Mud Tanks - Two Tank System, Rounded Bottom, 560 Barrels with Electric Agitators

Shaker – Derrick 503 Type Linear Motion

Desander - Derrick, (2) 12" Cones with Mission Magnum 5" x 6" Centrifugal Pump w/75 HP Electric Motor

Desilter - Derrick, (12) 4" Cones with Mission Magnum 5" x 6" Centrifugal Pump w/75 HP Electric Motor

Degasser – Derrick Drilco type

Oilfield Instrumentation Basic Services

281 Barrel Drill Water Tank

Revised 9/19/23